## Slide 1: LIMITING IMPERVIOUS SURFACE COVERAGE USING POROUS TECHNOLOGIES
Presented By:
RICHARD L. SNYDER, CPESC
RESOURCE CONSERVATIONIST
DAUPHIN COUNTY CONSERVATION DISTRICT

## Slide 2
“Financial and Other Support for this Project is Provided by the Pennsylvania Association of Conservation Districts, Inc. Through a Grant from the Pennsylvania Department of Environmental Protection Under Section 319 of the Clean Water Act, Administered by the U.S. Environmental Protection Agency.”

## Slide 3: WHAT IS PERVIOUS PAVEMENT?
PERMEABLE SURFACE COURSE
  Bituminous Asphalt
  Concrete
  Paver Blocks
  Reinforced Turf and Gravel Filled Grids
AASHTO #57 CHOKER COURSE
CLEAN, UNIFORMLY-GRADED STONE BED
  AASHTO #3
  Minimum Void Space of 40%
  Depth Varies – Generally 12” to 36”
NON-WOVEN GEOTEXTILE
UNCOMPACTED SUBGRADE

## Slide 4: POtEnTIal applications
RESIDENTIAL (LIMITED)
COMMERCIAL
ULTRA URBAN
INDUSTRIAL
RETROFIT
HIGHWAY / ROAD (LIMITED)

## Slide 5: STORMWATER FUNCTIONS
VOLUME REDUCTION = MEDIUM
RECHARGE = MEDIUM
PEAK RATE CONTROL = MEDIUM
WATER QUALITY = MEDIUM
  TSS = 85%
  TP = 85%
  N02 = 30%

## Slide 6: dEtAIled stORmwater functions
VOLUME REDUCTION
  Volume = Depth (ft) x Area (sf) x Void Space
  Infiltration Volume = Bed Bottom Area (sf) x Infiltration Rate (in/hr) x Infiltration Period (hr) x 1/12
PEAK RATE MITIGATION
WATER QUALITY IMPROVEMENT

## Slide 7: KEY DESIGN ELEMENTS
PERVIOUS PAVEMENT
  Primarily for Peak Rate Control
  Does NOT Address Water Quantity and / or Water Quality
  Storage is Short Duration
  Primary Use(s) is Rapidly Restored
  Minimize Safety Risks / Potential Property Damage / User Inconveniences
  Emergency Overflows
  Maximum Ponding Depths
  Flow Control Structures
  Adequate Surface Slope to Outlet
INFILTRATION BED
  Minimum 2’ of Renovating Soil
  Maximum Loading Ratio of 5:1 (Impervious Area:Infiltration Area)
  Natural, Uncompacted Soils with an Acceptable Infiltration Capacity
  Filled with Stone (or Alternative)
  Wrapped in Non-Woven Geotextile
  Nearly Level to Level Bottoms
  Positive Stormwater Overflow
  Protection from Sedimentation
  Perforated Pipe Network Along the Bottom for Distribution
  Open-Graded, Clean Stone with a Minimum 40% Void Space

## Slide 8: VARIATIONS / TYPES OF POROUS TECHNOLOGIES
BITUMINOUS ASPHALT
  Fines Screened / Reduced
  Single 3.5” Lift, Lightly Rolled to a Finished Depth of 2.5”
CONCRETE
  Reduced Number of Fines
  Coarser Appearance
PAVER BLOCKS
  Interlocking Units Filled with a Pervious Material
  Attractiveness / Aesthetics
REINFORCED TURF AND GRAVEL FILLED GRIDS
  Interlocking Structural Units, Containing Voids for Turf Grass Growth / Gravel
  Suitable for Both Traffic Loads and Parking
  Underlain by a Stone and / or Sand Drainage System

## Slide 9: DESIGN CONSIDERATIONS
EVALUATION FOR USE SHALL OCCUR EARLY IN THE DESIGN PROCESS
ORIENTATION OF PARKING BAYS ALONG EXISTING CONTOURS
  Significantly Reduces the Need for Cut / Fill
DO NOT PLACE ON RECENT FILL AND / OR COMPACTED FILL
  Grade Adjustments shall be Done with Stone Subbase Material
DO NOT COMPACT BED BOTTOM
STONE SUBBASE MATERIAL PLACED IN LIFTS, AND LIGHTLY ROLLED
STONE BED MAY BE USED AS A SEDIMENT BASIN / TRAP
  Reduces Overall Site Disturbance
  12” Buffer Between Sediment Basin / Trap Bottom and Final Bed Bottom Elevation
  Sediment shall be Removed as Part of Sediment Basin / Trap Conversion

## Slide 10: DESIGN CONSIDERATIONS (CONT.)
NEARLY LEVEL TO LEVEL BED BOTTOM
  Sloped Bed Bottom Creates Both Ponding and Reduced Distribution
OVERFLOW SYSTEM
  Inlet Boxes are Cost-Effective Overflow Structures
ABLE TO CONVEY / MITIGATE PEAK RUNOFF FROM LESS-FREQUENT, MORE-INTENSE STORMS
  Outlet Control Structure (i.e. Modified Inlet Box with Both an Internal Weir and a Low-Flow Orifice)
  Specific Design will Vary
BOTH STONE BED AND OVERFLOW SYSTEM MAY BE DESIGNED / EVALUATED SIMILAR TO A DETENTION BASIN
  Demonstrates Mitigation of Peak Runoff

## Slide 11: DESIGN CONSIDERATIONS (CONT.)
INTERNAL WEIR WITHIN AN INLET BOX / OVERFLOW STRUCTURE
  Maximizes Water Level in Stone Bed
  Provides Sufficient Cover for Overflow System
PERFORATED PIPES ALONG BED BOTTOM
  Evenly Distribute Runoff Over Entire Bed Bottom
  Connect Appurtenant Structures (i.e. Cleanouts, Inlets Boxes, Etc.)
  Lay Flat Along Bed Bottom
  May Provide Additional Storage Volume
ROOF LEADERS / AREA INLETS MAY BE CONNECTED
  Pre-Treatment is Recommended
LOCATED WITHIN IMMEDIATE PROJECT AREA
EROSION AND SEDIMENTATION CONTROL IS CRITICAL
  Surface Sediment Removed Via Vacuum Sweeper
  Do NOT Power-Wash Surface Sediment into Stone Bed

## Slide 12: DEsIGn consideRAtions (cont.)
STONE BED PLACED ON A SLOPE
  Benching / Terracing
STONE BED
  12” to 36” Deep
  Clean, Uniformly-Graded AASHTO #3 with Approximately 40% Void Space
  Sized to Mitigate Increased Runoff Volume from a 2-Year / 24-Hour Storm
ALTERNATIVE SUBSURFACE STORAGE PRODUCTS
  Proprietary, Interlocking Plastic Units
  Greater Storage Capacity than AASHTO #3
  Increased Cost
BACK-UP METHOD FOR RUNOFF TO ENTER STONE BED
  Uncurbed Lots – Unpaved 2’ Wide Stone Edge Drain
  Curbed Lots – Inlets with Pre-Treatment Devices

## Slide 13: DEsIgn considerations (cont.)
STONE BED MAY BE DESIGNED TO SLOWLY DISCHARGE TO ADJACENT WETLANDS AND / OR BIORETENTION AREAS
  Areas with Poorly Draining Soils
STONE BED LINED TO PREVENT INFILTRATION
  Industrial Sites with Contaminated Soils
PRE-TREATMENT DEVICES
  Threat of Spills and / or Groundwater Contamination
SEAL COATING AND / OR OVERPAVING
  Lack of Awareness

## Slide 14: CONSTRUCTION SEQUENCE
INSTALLATION / CONSTRUCTION SHALL BE NEAR THE END
STONE BED EXCAVATED TO FINAL GRADE
DO NOT COMPACT EXISTING SUBGRADE
UNWANTED FINES / SATURATED SOILS REMOVED WITH LIGHT EQUIPMENT, THEN SCARIFIED 6” MINIMUM
EARTHEN BERMS INSTALLED / CONSTRUCTED
GEOTEXTILE PLACED
  Adjacent Strips Overlap 16” Minimum
  Secured 4’ Minimum Outside of Stone Bed
STONE BED PLACED
  8” Lifts and Lightly Compacted
  Topped with a Choker Base Course (1+” AASHTO #57)
POROUS TECHNOLOGY INSTALLED
  Full Permeability Tested by Applying CLEAN Water at 5gpm

## Slide 15: LONG-TERM OPERATION AND MAINTENANCE
PRIMARY GOAL = TO PREVENT CLOGGING BY FINES
VACUUMED BIANNUALLY WITH COMMERCIAL CLEANING UNITS
  Pavement Washing Systems / Compressed Air Units are NOT Recommended
TRIBUTARY INLET BOXES CLEANED BIANNUALLY
ADJACENT VEGETATED / LANDSCAPED AREAS MAINTAINED SEMIANNUALLY
TRASH / LITTER / DEPOSITED SOIL REMOVED, PROPERLY DISPOSED
SPECIAL MAINTENANCE CONSIDERATIONS
  Winter Maintenance
  Repairs (i.e. Potholes, Settling, Etc.)
  NO, NO, NO…Seal Coating

## Slide 16: COST ISSUES
PERVIOUS ASPHALT
  10% to 20% Higher than Standard Asphalt per Unit Area
  Appropriate Comparison??
PERVIOUS CONCRETE
  More Expensive than Pervious Asphalt
  Increased Labor / Installation Experience
PERMEABLE INTERLOCKING CONCRETE PAVEMENT BLOCKS
  Varies by Type / Manufacturer
$2,000 TO $2,500 / PARKING SPACE (2005)

## Slide 17: Q&A / PROGRAM EVALUATION