## Slide 1: Rain gardens: effective Post-Construction stormwater management BMPs
Written by: Richard L. Snyder, CPESC
Resource Conservationist
Dauphin County Conservation District

## Slide 2: “Financial and Other Support for this Project is Provided by the Pennsylvania Association of Conservation Districts, Inc. Through a Grant from the Pennsylvania Department of Environmental Protection Under Section 319 of the Clean Water Act, Administered by the U.S. Environmental Protection Agency.”

## Slide 3: Definition
a.k.a. Bioretention / Recharge Garden / Bioretention Bed
An Excavated Shallow Surface Depression Planted with Specially Selected Native Vegetation to Treat and Capture Runoff
  Tolerant of Hydrologic Variability, Salts, and Environmental Stress
  Deep Rooted Perennials and Trees

## Slide 4: Potential Applications
Residential
Commercial
Urban
Industrial
Retrofit
Highway / Road
Institutional

## Slide 5: Stormwater Functions
Volume Reduction = Medium
Recharge = Medium to High
Peak Rate Control = Low to Medium
Water Quality = Medium to High
  TSS = 85% Reduction
  TP = 85% Reduction
  N03 = 30% Reduction
Thermal Impact Reduction
Enhance Evapotranspiration
Enhance Aesthetics
Provide Habitat

## Slide 6: Volume Reduction
Storage Volume = Surface Storage Volume (CF) + Lesser of Either Infiltration Volume (CF) or Sub-Surface Storage Volume (CF)
  Surface Storage Volume = Bed Area (ft2) x Average Design Water Depth
    Should be at Least 50% of the Storage Volume
  Infiltration Volume = Bed Bottom Area (ft2) x Design Infiltration Rate (in/hr) x Infiltration Period (hr) x 1/12
  Sub-Surface Storage Volume = Bed Bottom Area (ft2) x Modified Soil Bed Depth (ft) x Void Space (%)

## Slide 7: Key Design Elements
Flexible in Both Size and Infiltration (Adaptability)
  Moderate Infiltration Rates (> 0.1 in/hr)
In General, Ponding Depths Limited to 12”-
  Aesthetics
  Safety
  Rapid Draw Down
Deep Rooted Perennials and Trees
Native Vegetation Tolerant of Hydrologic Variability, Salts, and Environmental Stress
Soil Modified with Compost
Stable Inflow / Outflow Conditions
Provide Positive Overflow
Long-Term Operation and Maintenance

## Slide 8: Primary Components
Pre-Treatment (Optional)
  Vegetated Buffer Strip (Sheet Flow)
  Cleanout
  Water Quality Inlet
Flow Entrance (Varies per Site Use)
  Non-Erosive Inflow Velocity(s)
Ponding Area
Plant Material
Organic Layer and / or Mulch
  Shredded Wood Mulch
  Compost or Leaf Mulch (Preferred)
Planting Soil / Volume Storage Bed
Positive Overflow
  Domed Riser, Inlet, Weir Structure, Etc.
  Underdrain (Infiltration Rate < 0.1 in/hr)

## Slide 9: Sizing Criteria
Surface Area Depends upon Storage Volume Requirements
  Maximum Loading Ratio = 5:1 (Impervious Area:Infiltration Area)
Gradual Surface Side Slopes
  Recommended Maximum 3:1 (2:1 may be Acceptable for “Tight” Areas)
Surface Ponding Depth 6”-
  Empty Within 72 Hours
Ponding Area can be Supplemented with Sub-Surface Storage / Infiltration Bed
Planting Soil Depth
  18”+ with Herbaceous Plant Species
  Increased with Trees and / or Woody Shrubs

## Slide 10: Plant Material
Proper Selection
  Native Floodplain Species are Best Suited
Shrubs and Trees are Recommended
  Mimimum of 3 Species of Each
  Rate of 700 Shrubs per Acre and 300 Trees per Acre
  Shrub to Tree Ratio = 2:1 to 3:1
Planting Periods Vary
  Shrubs and Trees Planted from Mid-March to the End of June and / or Mid-September to Mid-November

## Slide 11: Organic Layer and / or Mulch
Maximum 2” to 3”
  Shredded Wood Mulch
  Compost or Leaf Mulch
Uniformly Applied Immediately After Shrubs and Trees
Avoid Wood Chips Due to Floating

## Slide 12: Planting Soil
Loam Soil
Modified with Compost / Composted Organic Material
  20% to 30% Compost
  70% to 80% Topsoil
Installed 4” Deeper than the Largest Root Ball

## Slide 13: Volume Storage Soils
pH Between 5.5 and 6.5
Clay Content < 10%
Free of Both Toxic Substances and Unwanted Plant Material
Organic Matter Content 5% to 10%
  Additional Organic Matter can be Added to Increase Water Holding Capacity

## Slide 14: Cross Sections / Details

## Slide 15: Construction Sequence
Install Temporary Sediment Control BMPs
Complete Site Grading
  Includes Construction of Flow Entrances
Stabilize Site Grading Within the LOD, Except for the Rain Garden Area
  If the Rain Garden Area is Used as a Temporary Sediment Trap, then the Finished Elevation of the Rain Garden is 12” Lower than the Bottom Elevation of the Sediment Trap
Excavate Rain Garden Area
  Scarify Existing Soil – NO, NO, NO…Compaction!!!
Backfill Rain Garden Area with Modified Soil
Presoak Planting Soil Prior to Planting Vegetation
Complete Final Grading of Rain Garden Area
Plant Vegetation
Mulch
Install Temporary Sediment Control BMPs at Flow Entrances

## Slide 16: Long-Term Operation and Maintenance
Pruning and Weeding of Plant Material
Annual Detritus Removal
Respread Mulch when Erosion is Evident
Replenish Mulch as Needed
Replace Mulch Once Every 2 to 3 Years
Bi-Annual Inspections for Sediment Build-Up, Erosion, Vegetative Conditions, Etc.
Watering During Periods of Extended Drought

## Slide 17: Cost Issues
Rain Garden Construction Cost < Landscape Area Net Cost
May Decrease the Cost for Stormwater Conveyance Systems
Pennsylvania Stormwater BMP Manual (December 2006)
  $5 to $7 / ft3 of Storage
Three Rivers Rain Garden Alliance (2009)
  DIY -- $3 to $5 /ft2
  Professional Design / Build -- $10 to $15 / ft2
  Plant Material is the Biggest Cost
Philadelphia Water Department (02/25/2016)
  $17 / ft2

## Slide 18: Q&A / Program Evaluation